## Slide 1
COLLEGE CAMPUS NETWORK
Cisco Cybersecurity Engineer Track
Presented To DEPI
Using Cisco Packet Tracer
22, Oct 2024

## Slide 2
About us
4th year engineering student specialized in information technology and communication engineering
Laila Sharkawy
Laila Sharkawy
Lailasharkawy21@gmail.com
We are interns at DEPI in Cisco Cybersecurity Track, group ONL1_ISS1_S2E.
In
Hager Hamdy
Fresh graduate, Faculty of computers and Artificial Intelligence
Hager Hamdy
Hagerhamdy632002@gmail.com
In
Bassma Mohamed
4th year computer and information student
Bassma Mosa
bassmamosa2@gmail.com
In
Ashrakat Rashwan
4th year engineering student specialized in information technology and communication engineering
Ashrakat Rashwan
ashrakatrashwan@gmail.com
In

## Slide 3
Content
Introduction
Network Design
Network Topology
Network Devices
Initial configuration scripts
Final Testing
VLAN and Inter-VLAN
VLANs Table
VLAN configuration
Network Security

## Slide 4
Introduction
This project involves the design, implementation, and security of a network infrastructure for a college campus using Cisco Packet Tracer. The campus network must support multiple users, including students, faculty, and administrative staff, while ensuring secure and efficient connectivity across various buildings and departments.

## Slide 5
The project will be completed in four phases:
Network Design and Configuration: Developing the network topology and configuring IP addressing and devices.
01
VLAN and Inter-VLAN Routing: Setting up VLANs to segment different user groups and configuring inter-VLAN routing for seamless communication.
02
Network Security Implementation: Applying security measures such as ACLs, port security, and firewalls to protect sensitive data and ensure network integrity.
03
Final Testing and Reporting: Testing the network’s functionality, performance, and security, and documenting the results for presentation.
04

## Slide 6
Network Design
and Configuration

## Slide 7
Network Topology

## Slide 11
List of Network Devices:
01
End Devices:
PCs
Printers
Servers such as (Web server, FTP server and Email server.

## Slide 12
List of Network Devices:
01
02
Intermediary Devices:
Layer 3 Switch (3650-24PS)
Switch 2960
Router 2911
End Devices:
PCs
Printers
Servers such as (Web server, FTP server and Email server.

## Slide 13
Initial configuration scripts for :
Router>en
Router#conf t
Enter configuration commands, one per line. End with CNTL/Z.
Router(config)#int gig0/0
Router(config-if)#no sh
Router(config-if)#
%LINK-5-CHANGED: Interface GigabitEthernet0/0, changed state to up
Router(config-if)#int se0/1/0
Router(config-if)#no sh
CAMPUS ROUTER
%LINK-5-CHANGED: Interface Serial0/1/0, changed state to down
Router(config-if)#do wr
Building configuration...
[OK]
Router(config-if)#in se0/1/0
Router(config-if)#clock rate 64000
Router(config-if)#do wr
Building configuration...
[OK]
Router>en
Router#conf t
Enter configuration commands, one per line. End with CNTL/Z.
Router(config)#int se0/1/0
Router(config-if)#ip address 10.10.10.1 255.255.255.252

## Slide 14
Initial configuration scripts for :
CLOUD
Router>EN
Router#CONF T
Enter configuration commands, one per line. End with CNTL/Z.
Router(config)#INT gig0/0
Router(config-if)#no sh
Router(config-if)#
%LINK-5-CHANGED: Interface GigabitEthernet0/0, changed state to up
%LINEPROTO-5-UPDOWN: Line protocol on Interface GigabitEthernet0/0, changed state to up
Router(config)#int se0/1/0
Router(config-if)#ip address 10.10.10.2 255.255.255.252
Router(config-if)#ex
Router(config)#do wr
Building configuration...
[OK]
Router(config)#int gig0/0
Router(config-if)#ip address 20.0.0.1 255.255.255.252
Router(config-if)#ex
Router(config)#ip route 192.168.1.0 255.255.255.0 se0/1/0
%Default route without gateway, if not a point-to-point interface, may impact performance
Router(config-if)#int se0/1/0
Router(config-if)#no sh
Router(config-if)#
%LINK-5-CHANGED: Interface Serial0/1/0, changed state to up
Router(config-if)#do wr
Building configuration...
[OK]
Router>en
Router#conf t
Enter configuration commands, one per line. End with CNTL/Z.

## Slide 15
IP Addressing Scheme:
DHCP was deployed to simplify IP address management by automatically assigning IP addresses to devices within the network. Each VLAN has its own IP address range.
The core router was configured with DHCP pools for each VLAN. Devices connected to each VLAN automatically receive an IP address within their respective range, simplifying network management and reducing the risk of IP address conflicts.
DHCP Configuration:
Router(config)#service dhcp
Router(config)#ip dhcp pool admin-pool
Router(dhcp-config)#network 192.168.1.0 255.255.255.0 Router(dhcp-config)#default-router 192.168.1.1 Router(dhcp-config)#dns-server 192.168.1.1
Router(dhcp-config)#ex

## Slide 16
2. VLAN and
Inter-VLAN Routing

## Slide 17
VLAN Configuration scripts :
L3 SWITCH
Switch>en
Switch#config t
Switch(config)#vlan 10
Switch(config-vlan)#name admin
Switch(config-vlan)#exit
Switch(config)#vlan 20
Switch(config-vlan)#name hr
Switch(config-vlan)#exit

## Slide 18
Statistics
Revenue Growth
80%
Lorem ipsum dolor sit amet, consectetur adipiscing elit. Integer nec sagittis mauris, vitae vehicula urna. Curabitur ultrices urna sit amet magna ultricies ornare. Curabitur ligula.
Return on Investment
10%
Customer Acquisition Cost
20%
Customer Satisfaction
75%
VLAN Name | VLAN ID | Subnet (CIDR) | Gateway (Router IP) | DHCP Range
admin | 10 | 192.168.1.0/24 | 192.168.1.1/24 | 192.168.1.2- 192.168.1.254
hr | 20 | 192.168.2.0/24 | 192.168.2.1/24 | 192.168.2.2- 192.168.2.254
finance | 30 | 192.168.3.0/24 | 192.168.3.1/24 | 192.168.3.2- 192.168.3.254
buisness | 40 | 192.168.4.0/24 | 192.168.4.1/24 | 192.168.4.2- 192.168.4.254
engineering | 50 | 192.168.5.0/24 | 192.168.5.1/24 | 192.168.5.2- 192.168.5.254
arts | 60 | 192.168.6.0/24 | 192.168.6.1/24 | 192.168.6.2- 192.168.6.254
studentlabs | 70 | 192.168.7.0/24 | 192.168.7.1/24 | 192.168.7.2- 192.168.7.254
it | 80 | 192.168.8.0/24 | 192.168.8.1/24 | 192.168.8.2- 192.168.8.254
VLANs Table:

## Slide 19
VLAN Configuration scripts :
For each switch ( taking into account the VLANs differing)
Switch>en
Switch#conf t
Enter configuration commands, one per line. End with CNTL/Z.
Switch(config)#int range fa0/1-24
Switch(config-if-range)#switchport mode access
Switch(config-if-range)#switchport access vlan 10
% Access VLAN does not exist. Creating vlan 10
Switch(config-if-range)#do wr

## Slide 20
Inter-VLAN routing documentation : The same applies to the rest of the VLANs
CAMPUS ROUTER
Router>en
Router#conf t
Enter configuration commands, one per line. End with CNTL/Z.
Router(config)#int gig0/0.10
Router(config-subif)#
%LINK-5-CHANGED: Interface GigabitEthernet0/0.10, changed state to up
%LINEPROTO-5-UPDOWN: Line protocol on Interface GigabitEthernet0/0.10, changed state to up
Router(config-subif)#encapsulation dot1Q 10
Router(config-subif)#ip address 192.168.1.1 255.255.255.0
Router(config-subif)#ex
Router(config)#int gig0/0.20
Router(config-subif)#
%LINK-5-CHANGED: Interface GigabitEthernet0/0.20, changed state to up
%LINEPROTO-5-UPDOWN: Line protocol on Interface GigabitEthernet0/0.20, changed state to up
Router(config-subif)#encapsulation dot1Q 20
Router(config-subif)#ip address 192.168.2.1 255.255.255.0
Router(config-subif)#ex

## Slide 21
VLAN Trunk Configuration :
L3 SWITCH
Switch(config)#int g1/0/1
Switch(config-if)#sw
Switch(config-if)#switchport mode trunk
Switch(config-if)#
%LINEPROTO-5-UPDOWN: Line protocol on Interface GigabitEthernet1/0/1, changed state to down
%LINEPROTO-5-UPDOWN: Line protocol on Interface GigabitEthernet1/0/1, changed state to up
Switch(config-if)#no shut
Switch(config-if)#exit

## Slide 22
3. Network Security Implementation

## Slide 23
Network Security Implementation :
Security Configuration :
Switch>
Switch>en
Switch#conf t
Enter configuration commands, one per line. End with CNTL/Z.
Switch(config)#hostna
Switch(config)#hostname s-engineering
s-engineering(config)#line con
s-engineering(config)#line console 0
s-engineering(config-line)#pass
s-engineering(config-line)#password ciscoroot
s-engineering(config-line)#login
s-engineering(config-line)#exit
s-engineering(config)#cry
s-engineering(config)#crypto k
s-engineering(config)#crypto key g
s-engineering(config)#crypto key generate r
s-engineering(config)#crypto key generate rsa
% Please define a domain-name first.
s-engineering(config)#ip domain-n
s-engineering(config)#ip domain-name project.com
s-engineering(config)#crypto key generate rsa
The name for the keys will be: s-engineering.project.com
Choose the size of the key modulus in the range of 360 to 4096 for your
General Purpose Keys. Choosing a key modulus greater than 512 may take
a few minutes.
How many bits in the modulus [512]: 1024
% Generating 1024 bit RSA keys, keys will be non-exportable...[OK]

## Slide 24
Network Security Implementation :
SSH security Configuration :
s-engineering(config)#ip s
*Mar 2 1:19:49.895: %SSH-5-ENABLED: SSH 1.99 has been enabled
s-engineering(config)#ip ssh
s-engineering(config)#ip ssh v
s-engineering(config)#ip ssh version 2
s-engineering(config)#line vty 0 4
s-engineering(config-line)#login local
s-engineering(config-line)#trans
s-engineering(config-line)#transport input ssh
s-engineering(config-line)#exit
s-engineering(config)#username admin secret ciscorootssh

## Slide 25
Network Security Implementation :
Port security Configuration :
s-engineering(config)#interface range fa0/1-24
s-engineering(config-if-range)#switchport mode access
s-engineering(config-if-range)#switchport port-security maximum 2
s-engineering(config-if-range)#switchport port-security violation restrict
s-engineering(config-if-range)#switchport port-security mac-address sticky
s-engineering(config-if-range)#exit

## Slide 26
Network Security Implementation :
ACL Rules :
To prevent external access from the internet to FTP server located in the 192.168.8.0/24 network
Block FTP traffic (port 21, for control) from the internet to the FTP server network (192.168.8.0/24).
Block FTP data traffic (port 20, for data transfer) as well.
access-list 120 deny tcp any 192.168.8.0 0.0.0.255 eq 21
access-list 120 deny tcp any 192.168.8.0 0.0.0.255 eq 20
Permit other legitimate traffic from the internet (such as web traffic or other services):
access-list 120 permit tcp any any eq 80 # HTTP (optional)
access-list 120 permit tcp any any eq 443 # HTTPS (optional)
access-list 120 permit ip any any # Permit all other traffic

## Slide 27
Network Security Implementation :
ACL Configuration :
r-basic(config)#access-list 120 deny tcp any 192.168.8.0 0.0.0.255 eq 21
r-basic(config)#access-list 120 deny tcp any 192.168.8.0 0.0.0.255 eq 20
r-basic(config)#access-list 120 permit tcp any any eq 80
r-basic(config)#access-list 120 permit tcp any any eq 443
r-basic(config)#access-list 120 permit ip any any
r-basic(config)#in
r-basic(config)#interface g
r-basic(config)#interface gigabitEthernet 0/0.80
r-basic(config-subif)#ip access-group 120 in

## Slide 28
4. Final Testing and
Reporting

## Slide 29
IP address configuration using DHCP

## Slide 30
Ping Test:

## Slide 31
Ping Test:

## Slide 32
Traceroute:

## Slide 33
In conclusion, this project successfully achieved the objective of designing, building, and securing a small network. Through the step-by-step implementation process, we were able to:
Establish a robust network infrastructure using Cisco devices with proper configuration of VLANs, IP addressing, and inter-VLAN routing to ensure efficient and segmented communication within the network.
Implement essential security features, including Access Control Lists (ACLs) and port security.
Verify the network's functionality.

## Slide 34
Suggestions for Future Enhancements:
Integrating advanced security measures such as firewalls and intrusion detection systems (IDS) can further strengthen the network's defense.
Implementing Quality of Service (QoS) mechanisms to prioritize critical traffic and improve network performance under high load.

## Slide 35
THANK YOU!